## Slide 1: RVI – V2X Board

## Slide 2
Technical Purpose
Send data from any vehicle
over the air
to the outside world

## Slide 3
Strategic Purpose
Bring the creativity of the startup community to the OEMs by providing a consumer-grade development platform closely linked to the automotive eco system

## Slide 4
V2X Board
Overview
V2X Board [OSS Hardware by JLR] Integrates GPS, CAN, OBD-II, 2G/3G, and accelerometer data into a single USB connection
Raspberry Pi Data Acquisition from V2X board. V2X board M2M modem used to communicate with backend
Backend Server Receives and analyses reports transmitted from RasPi / V2X board combination
CAN
GPS
RasPi
RVI DAQ
OBD2
Backend Server
RVI

## Slide 5
Consumer
Speed retrieved by V2X board from OBD-2
V2X board forwards speed to RasPi
RasPi forwards speed to RVI
Big data server processes data
RVI uses V2X modem to forward to big data
Comparing two stacks
V2X
Consumer
Big Data Server
OBD-II
SPD=140
RVI
RPi
IVI
OEM
CAN
SPD=140
TCU
RVI
RVI
OEM
Speed retrieved by IVI from CAN bus
IVI forwards speed to Telematics Control Unit
TCU forwards data to RVI
Big data server processes data
RVI uses TCU modem to forward to big data

## Slide 6
2G/3G Modem
Provides communication to the outside world
GPS
Provides positioning for on-board apps
Accelerometer
Aids navigation and situational awareness
Single USB connection
Clean data pipe and power between V2X and Raspberry Pi
Power Management
V2X board can wake up Raspberry Pi at a specific time, on OBD-II activation, or on a received SMS
Open Source and Hardware
All hardware design and associated software is open source licensed
Feature Benefits

## Slide 7
Package content
V2X Board with SIM
Turn-key system with mobile subscription
RasPi RVI
Specific RVI configured to use M2M modem of V2X board
Python Libraries
RasPi libraries enabling python-based RVI services to interact with V2X board
Sample RasPi Service
Sample service to read OBD-II data and export it, real time, to the backend server
Backend Server Account
Pre-provisioned account to receive V2X-originated data
Sample Android app
Android app to retrieve and display real-time V2X data from backend server

## Slide 8: Thank You
Magnus Feuer Lead System Architect – Open Software Initiative
mfeuer@jaguarlandrover.com
+1-949-294 7871